## Slide 1: Information Security – Theory vs. Reality 0368-4474, Winter 2015-2016 Lecture 6: Physical Side Channel Attacks on PCs
Guest lecturer: Lev Pachmanov

## Slide 2: Side channel attacks
electromagnetic
acoustic
probing
optical
power
CPU architecture
chassis potential

## Slide 3: Traditional side channel attacks methodology
Grab/borrow/steal device
Find key-dependent instruction
Record emanations using high-bandwidth equipment (> clock rate , PC: >2GHz)
Obtain traces
Signal and cryptanalytic analysis
Recover key
for i=1…2048
sqr(…)
if key[i]=1
mul(…)
Hard for PCs

## Slide 4: Traditional side channel attacks methodology
Grab/borrow/steal device
Find key-dependent instruction
Record emanations using high-bandwidth equipment (> clock rate , PC: >2GHz)
Obtain traces
Signal and cryptanalytic analysis
Recover key
Hard for PCs

## Slide 5: Traditional side channel attacks methodology
Grab/borrow/steal device
Find key-dependent instruction
Record emanations using high-bandwidth equipment (> clock rate , PC: >2GHz)
Obtain traces
Signal and cryptanalytic analysis
Recover key
Hard for PCs
Not handed out
vs.
Measuring a 2GHz PC requires expansive and bulky equipment (compared to a 100
MHz smart card)
vs.
100,000$
1,000$
Complex electronics running complicated software (in parallel)
vs.

## Slide 6: Our results
Channels for attacking PCs
  Ground potential (chassis and others)
  Power
  Electromagnetic
  Acoustic
Exploited via low-bandwidth cryptanalytic attacks
  Adaptive attack (50 kHz bandwidth) [Genkin Shamir Tromer ‘14]
  Non-adaptive attacks (1.5 MHz bandwidth) [Genkin Pipman Tromer ‘14] [Genkin Pachmanov Pipman Tromer ‘15]
Common cryptographic software
  GnuPG 1.4.13-1.4.16 (CVE 2013-4576, 2014-3591, 2014-5270)
  RSA and ElGamal, various implementations
  Worked with GnuPG developers to mitigate the attacks
Applicable to various laptop models

## Slide 7: Chassis-potential channel

## Slide 8: Ground-potential analysis
Attenuating EMI emanations “Unwanted currents or electromagnetic fields? Dump them to the circuit ground!” (Bypass capacitors, RF shields, …)
Device is grounded, but its “ground” potential fluctuates relative to the mains earth ground.
Computation
affects currents and EM fields
dumped to device ground
connected to conductive chassis
Key = 101011…

## Slide 9: Connecting to the chassis

## Slide 10: Demo: distinguishing instructions
Key = 101011…

## Slide 11: Distinguishing various CPU operations
frequency (2-2.3 MHz)
time (10 sec)

## Slide 12: Low-bandwidth leakage of RSA

## Slide 13: Definitions (RSA)
Key setup
sk: random primes , private exponent
pk: , public exponent
Encryption
Decryption
A quicker way used by most implementations
Obtain using Chinese Remainder Theorem

## Slide 14: GnuPG RSA key distinguishability
mod
mod
frequency (1.9-2.4 MHz)
time (0.8 sec)
Can distinguish between:
  Decryptions and other operations
  Two exponentiations (mod , mod )
  Different keys
  Different primes

## Slide 15: Key extraction

## Slide 16: GnuPG modular exponentiation
modular_exponentiation(c,d,p){
m=1
for i=n to 1 do
m = m2 mod p
t = m*c mod p //always mult
if d[i]==1 then
m=t
return m
}
Q: Why always compute then conditionally copy?
A: This is a side channel countermeasure meant to protect
no key dependent operation to measure

## Slide 17: GnuPG modular exponentiation
modular_exponentiation(c,d,p){
m=1
for i=n to 1 do
m = m2 mod p
t = m*c mod p //always mult
if d[i]==1 then
m=t
return m
}
depends on both and
is squard in next iteration of the main loop
craft to affect the squaring in the next loop iteration, based on
measure changes inside squaring operation and obtain
  2GHz CPU speed vs. 1.5MHz measurements
can only see drastic changes inside squaring operation
  Idea: leakage self-amplification
  abuse algorithm’s own code to amplify its own leakage!
  Craft suitable cipher-text to affect the inner-most loop
  Small differences in repeated inner-most loops cause a big overall difference in code behavior
Notes: לחבר את זה לCPA – גם פה מנצלים בעיה במימוש

## Slide 18: Non-adaptive key extraction (similar to [Yen, Lien, Moon and Ha 05])
modular_exponentiation(c,d,p){
m=1
for i=n to 1 do
m = m2 mod p
t = m*c mod p //always mult
if d[i]==1 then
m=t
return m
}
karatsuba_sqr( m ){
…
basic_sqr( x )
…
}
basic_sqr( x ){
…
}
if( x[j]==0)
y = 0 else y = x[j]*x
If then
so bits of are “random”.
If then so bits of have many zeros.
0/$
x7
Many zeros or
random looking,
based on
x27
repeated 189 times per bit of
~0.2ms of measurement per bit of

## Slide 19: A chosen ciphertext attack
Non-adaptive ciphertext choice (similar to [YLMH05]):
RSA:
ElGamal:
Overall attack performance:
Algorithm | Attack type | # ciphertexts | Time | BW | Cipher | Ref
Sqr-and- always-mlt | Non-adaptive chosen ciphertext | 1 | 3 sec | 2 MHz | ElGamal, RSA | [GPT14]

## Slide 20: A chosen ciphertext attack
Non-adaptive ciphertext choice (similar to [YLMH05]):
RSA:
ElGamal:
Overall attack performance:
Algorithm | Attack type | # ciphertexts | Time | BW | Cipher | Ref
Sqr-and- always-mlt | Non-adaptive chosen ciphertext | 1 | 3 sec | 2 MHz | ElGamal, RSA | [GPT14]
Sliding / fixed window | Non-adaptive chosen ciphertext | (usually 8 or 16) | 30 sec | 2 MHz | ElGamal, RSA | [GPPT15]
Algorithm | Attack type | # ciphertexts | Time | BW | Cipher | Ref
Sqr-and- always-mlt | Non-adaptive chosen ciphertext | 1 | 3 sec | 2 MHz | ElGamal, RSA | [GPT14]
Sliding / fixed window | Non-adaptive chosen ciphertext |  | 30 sec | 2 MHz | ElGamal, RSA | [GPPT15]

## Slide 21: A chosen ciphertext attack
Non-adaptive ciphertext choice (similar to [YLMH05]):
RSA:
ElGamal:
Overall attack performance:
Algorithm | Attack type | # ciphertexts | Time | BW | Cipher | Ref
Sqr-and- always-mlt | Non-adaptive chosen ciphertext | 1 | 3 sec | 2 MHz | ElGamal, RSA | [GPT14]
Sliding / fixed window | Non-adaptive chosen ciphertext | (usually 8 or 16) | 30 sec | 2 MHz | ElGamal, RSA | [GPPT15]
Sqr-and- always-mlt | Adaptive chosen ciphertext |  | 1 hour | 50 kHz | RSA | [GST14]
Algorithm | Attack type | # ciphertexts | Time | BW | Cipher | Ref
Sqr-and- always-mlt | Non-adaptive chosen ciphertext | 1 | 3 sec | 2 MHz | ElGamal, RSA | [GPT14]
Sliding / fixed window | Non-adaptive chosen ciphertext |  | 30 sec | 2 MHz | ElGamal, RSA | [GPPT15]
Sqr-and- always-mlt | Adaptive chosen ciphertext |  | 1 hour | 50 kHz | RSA | [GST14]

## Slide 22: A chosen ciphertext attack
Non-adaptive ciphertext choice (similar to [YLMH05]):
RSA:
ElGamal:
Overall attack performance:
Algorithm | Attack type | # ciphertexts | Time | BW | Cipher | Ref
Sqr-and- always-mlt | Non-adaptive chosen ciphertext | 1 | 3 sec | 2 MHz | ElGamal, RSA | [GPT14]
Sliding / fixed window | Non-adaptive chosen ciphertext | (usually 8 or 16) | 30 sec | 2 MHz | ElGamal, RSA | [GPPT15]
Sqr-and- always-mlt | Adaptive chosen ciphertext |  | 1 hour | 50 kHz | RSA | [GST14]
Algorithm | Attack type | # ciphertexts | Time | BW | Cipher | Ref
Sqr-and- always-mlt | Non-adaptive chosen ciphertext | 1 | 3 sec | 2 MHz | ElGamal, RSA | [GPT14]
Sliding / fixed window | Non-adaptive chosen ciphertext |  | 30 sec | 2 MHz | ElGamal, RSA | [GPPT15]
Sqr-and- always-mlt | Adaptive chosen ciphertext |  | 1 hour | 50 kHz | RSA | [GST14]
Ciphertext injection
Send chosen ciphertexts via email (PGP/MIME). Decrypted by email client (e.g., Enigmail) automatically.

## Slide 23: Empirical results: ground-potential attacks

## Slide 24: Demo: RSA key extraction from chassis potential

## Slide 25: Reading the secret key (non-adaptive attack)
carrier
FM-modulated key
due to squaring of a random-looking /
mostly zero limb value of
Key = 101011…

## Slide 26: Reading the secret key (non-adaptive attack)
Acquire trace
Filter around carrier (1.7 MHz)
FM demodulation
Read out bits (“simple ground analysis”)
interrupt

## Slide 27: RSA and ElGamal key extraction in a few seconds using human touch (non-adaptive attack)
Key = 101011…

## Slide 28: Ground-potential analysis
Attenuating EMI emanations “Unwanted currents or electromagnetic fields? Dump them to the circuit ground!” (Bypass capacitors, RF shields, …)
Device is grounded, but its “ground” potential fluctuates relative to the mains earth ground.
Computation
affects currents and EM fields
dumped to device ground
connected to conductive chassis

## Slide 29: Ground-potential analysis
Attenuating EMI emanations “Unwanted currents or electromagnetic fields? Dump them to the circuit ground!” (Bypass capacitors, RF shields, …)
Device is grounded, but its “ground” potential fluctuates relative to the mains earth ground.
Computation
affects currents and EM fields
dumped to device ground
connected to conductive chassis
connected to shielded cables
Key = 101011…
Even when no data, or port is turned off.

## Slide 30: RSA and ElGamal key extraction in a few seconds using the far end of 10 meter network cable
works even if a firewall is present, or port is turned off
key= 101011…

## Slide 31: Empirical results: electromagnetic attacks

## Slide 32: Electromagnetic key extraction
Currents inside the target create electromagnetic waves.
Can be detected using an electromagnetic probe (e.g., a loop of cable).
target
attacker

## Slide 33: Portable Instrument for Trace Acquisition
Cost to build: ~300$

## Slide 34: Key extraction via commodity radio receiver

## Slide 35: Acoustic cryptanalysis

## Slide 36: Acoustic emanations from PCs
    Noisy electrical components in the voltage regulator
    Commonly known as “coil-whine’’ but also originates from capacitors
Bzzzzzz

## Slide 37: Experimental setup (example)
target
microphone
amplifier
attacker
digitizer

## Slide 38: Adaptive key extraction
Severe attenuation of high frequency signals.
Effective bandwidth of 50 kHZ
Cannot observe a single squaring
Make the entire decryption depend on a single attacked bit
Extreme version of self-amplification
Extract the prime bit-by-bit (adaptive chosen ciphertext)
Total #measurements: 2048 decryptions for RSA-4096 (~1 hour)

## Slide 39: An adaptive chosen-ciphertext attack
1111...1
1000…0
1
0
…
…
Bit-distinguisher oracle

## Slide 40: An adaptive chosen-ciphertext attack
Total #measurements:
Overall: 2048 decryptions for RSA-4096 (~1 hour)
Just q
Coppersmith lattice reduction: half the bits suffice
Error
correction
Bit distinguisher oracle

## Slide 41: GnuPG RSA decryption -
modular_exponentiation(c,d,q){
…
karatsuba_mult(m,c)
…
}
karatsuba_mult(m,c){
…
basic_mult(x,y)
…
}
basic_mult(x,y){
…
}
if (y[j]==0)
return 0 else return y[j]*x
x7
craft c such that
(for most ’s)
x19
x2048
Grand total:
272384 times
~0.5 sec of measurements

## Slide 42: Extracting (simplified)
If then ,
thus .
That is, has special structure.
If then , thus .
That is, is random looking.
and we now multiply by causing the bit-dependent leakage.

## Slide 43: Extracting
If then , thus .
That is, has special structure.
If then
, thus .
That is, is random looking.
and we now multiply by causing the bit-dependent leakage.

## Slide 44: Extracting (problem)
Single multiplication is way too fast for us to measure
Multiplication is repeated 2048 times (0.5 sec of data)

## Slide 45: Empirical results: acoustic attacks

## Slide 46: Distinguishing a key bit by a spectral signature
frequency
time
frequency
time
mod q
mod p
mod q
mod p

## Slide 47: Demo: key extraction

## Slide 48: Acoustic: results
RSA 4096-bit key extraction from 1 meter away using a microphone

## Slide 49: Acoustic: results
RSA 4096-bit key extraction from
10 meters away using a parabolic microphone

## Slide 50: Acoustic: results
RSA 4096-bit key extraction from 30cm away using a smartphone

## Slide 51: Countermeasures

## Slide 52: Countermeasures
Common suggestions
Shielding
  EM (Faraday cages), ground difficult and expensive
  Acoustic? Vents!
Add analog noise (expensive, correlations remain)
Parallel software load (inadequate, may help attacker)
Attacks rely on decryption of chosen ciphertexts.
Solution: ciphertext randomization use equivalent but random-looking ciphertexts
Negligible slowdown for RSA
x2 slowdown for ElGamal

## Slide 53: Effective countermeasure: ciphertext randomization (added in GnuPG 1.4.16)
Given a ciphertext :
Generate a random number and compute
Decrypt and obtain
Output
Works since thus:

## Slide 54
tau.ac.il/~tromer/acoustic CRYPTO’14 CVE 2013-4576
tau.ac.il/~tromer/handsoff CHES’14 CVE-2014-5270
tau.ac.il/~tromer/radioexp CHES’15 CVE-2014-3591